Golden Coast Cannabis
Lighting estimates

## summary:
State of Jefferson is a proxy for McCloud, golden coast is a proxy for San Mateo
my original estimate from this morning was based on 500 PAR minimum light, this estimate is based on 750 PAR minimum light. I added 500 PAR minimum light totals at bottom of this section as well.
Costs were based on $0.25 per kWh. If there is a substantial difference between power costs I should re-calculate costs based on more accurate rates.
monthy auxillary lighting costs

annual auxillary lighting costs are $438,286.76 for golden coast and $536,156.62 for state of Jefferson
the total number of lights in either location is 983 – something like $400,000.00 for lights
state of Jefferson costs $100,000 more a year for auxillary lighting than golden coast does at 750 PAR.
If we ran at 500 PAR minimum light the costs are $173,045.26 for golden coast and $222,689.39 for State of Jefferson. This is less than half the cost of 750 PAR but will result in a reduced yield. I don't know how reduced the yield will be but probably will be more than half. If we plan for 750 PAR and decide to run at something less then at least we have enough capacity and can comfortably find a sweet spot in the yield/lighting cost curve.

### definitions:
PAR:	photosynthetic available radiation, which is basically a count of photons per meter squared per second that provide energy for photosynthesis.

DLI: daily light integral, a measurement that represents the accumulated PAR in a 24 hour period.

Section: the way we've been discussing the greenhouse is in 2750 sq ft sections. 8 sections make the 22,000 sq ft flowering greenhouse, 2 sections are used for early flowering, 1 section is used for vegetative growth. We will also need 1600 sq ft for mothers and 1600 sq ft for strain development.

PAR requirement: as long as cannabis is provided with other factors such as CO2, nutrients, temperature in optimum ranges, it increases growth and yield up to about 1200 PAR, at about 750 PAR the increase in growth and yield starts to flatten out and approach diminishing return. High light intensity greenhouse crops grow well in 22 to 30 DLI or about 500 to 700 PAR. I provide enough lights to boost winter greenhouse DLI up to 32.4 which is the equivalent of 750 PAR per hour for 12 hours.

## calculations:
I am calculating lighting needs for two different locations, one representing a San Mateo location and the other representing a McCloud location
Using data from Purdue University extension on DLI for those two locations we get the following averages

DLI per month

This DLI data is for outdoor levels. Depending on glazing and sun angle DLI can be reduced from 40 to 70 percent. I am assuming glazing is set ideally for optimal winter transmission and calculating a 40 percent loss. 20% for glazing and 20% for structure

DLI minus glazing and structural loss
The conversion from DLI to PAR equivalence lighting is as follows: (DLI / 0.0864)/(24 hours / number of hours of light). For example: golden coast canopy in August will receive something like 30 DLI. This converts 694 PAR. In order to reach 750 PAR which is a DLI of 32.4, we will need to add 2.4 DLI or about 55 PAR (the strength of a florescent bulb at about 10 inches). With a target of 750 PAR these calculations will set 32.4 DLI as a minimum standard. This is very conservative in that light intensive greenhouse crops like tomatoes and peppers use 22 to 30 DLI. Earlier estimates were based on 22 DLI (500 PAR) but to be conservative (estimating on the high side) I'm increasing the minimum DLI to 32.4 (750 PAR)

Here is the additional light DLI needed to offset seasonal variations in DLI

Additional DLI needed
converting that to PAR needed for a 12 hour flower cycle and an 18 hour veg cycle (two graphs)

additional PAR needed for flower rooms (12 hours light)

additional PAR needed for vegetative growth (veg and mother)
A 1000 watt double ended HPS Gavita uses 1033 watts and produces 1751 PAR. With this we can calculate the minimum number of lights needed to provide additional enough additional light to produce 750 PAR. The light placement density needed is .32256 lights per square meter. Very close to one 1000 watt Gavita for every three square meters in flowering and strain development. For the 18 hour lights it's about one Gavita for every 5 square meters, this is less because the lights are on for 18 hours instead of 12.

Using this number of lights I can calculate watts per month per square meter.

flowering watts per month per square meter

watts per month per square meter for veg and mothers

One square foot = 0.092903 square meters.
A section of 2750 sq ft is 255.4834 square meters, I'll use 256 square meters per section.
For flowering space there are 10 sections + 1600 sq ft for strain development another 149 square meters for a total of 2709 square meters.

total flowering kWh per month for 10 sections + strain development

One section for veg is 256 sq meters and 1600 sq foot mother room at 149 sq meters is 405 square meters.

veg and mother kWh per month

And put them together

total kWh per month needed for auxillary lighting

using $0.25 per kWh for electrical costs gives us monthly costs

monthy auxillary lighting costs

annual auxillary lighting costs are $438,286.76 for golden coast and $536,156.62 for state of Jefferson
the total number of lights in either location is 983
state of Jefferson costs $100,000 more a year for auxillary lighting than golden coast does. Of course this is highly dependent on actual electrical rates.